## Slide 1: Adaptive Current Control Method
By Yaron Zimmerman
April 2025

## Slide 2: Motivation & Problem
DCBL coil resistance varies with temperature (up to 50%)
Affects closed-loop current control performance
Traditional PI controllers fail under low sample rates or fast dynamics

## Slide 3: Introduction for current control
O

## Slide 4: Model

## Slide 5: Why Estimation is Needed
Large resistance variations break traditional tuning
Online estimation allows dynamic gain adjustment

## Slide 6: Proposed Solution
Online estimation of coil resistance using Kalman Filters
Adaptive tuning of PI controller gain (kI)
Modeling based on coupled electrical and thermal dynamics

## Slide 7: Dynamics modeling

## Slide 8: State-Space Model
States: I, R, RE; Inputs: control voltage, speed
Includes process and measurement noise
Formulated for EKF/UKF estimation

## Slide 9: Non-linear state functions

## Slide 10: Approach Overview
Nonlinear state-space model with 3 states: current, resistance, env. Resistance
  ,
Use EKF and UKF for real-time estimation

## Slide 11: Extended Kalman Filter (EKF)
Linearizes model at each step
Prediction and correction steps
Discretization via Jacobians

## Slide 12: Extended Kalman Filter (EKF)

## Slide 13: Unscented Kalman Filter (UKF)
Statistical linearization via sigma points
Better performance with nonlinear systems
More robust during transients

## Slide 14: Unscented Kalman Filter (UKF)

## Slide 15: Unscented Kalman Filter (UKF)

## Slide 16: Simulation Setup
Square wave reference current input
Adaptive
Simulation parameters from paper

## Slide 17: Resistance Estimation Results
Both EKF and UKF estimate resistance accurately
UKF outperforms EKF in convergence and error margin

## Slide 18: Current Response Results
Improved current tracking after estimation convergence
Adaptive controller enhances system response

## Slide 19: Conclusions
Online estimation enables adaptive current control.
EKF and UKF are effective; UKF performs better.
Robust under dynamic conditions.
It may also be used to estimate the motor’s coil temperature.